## Slide 1: Implications of Decentralized Q-learning Resource Allocation in Wireless Networks

## Slide 2: Outline
Motivation
Stateless Q-learning
Scenario & System Model
Simulation Results
Conclusions

## Slide 3: Motivation

## Slide 4: Main Goal
Study the feasibility of achieving fair configurations that enhance the overall throughput in a decentralized way
Uncoordinated Wireless Networks (WNs) that compete for the same resources
Reinforcement Learning (RL),
more precisely a stateless variation of Q-learning
What?
In which context?
With which tools?

## Slide 5: Next-generation WNs
Future WNs will be characterized by high-density and chaotic deployments
Dense scenarios
High amount of devices that coexist (e.g., 1 user/m2)
Coexistence derives into performance issues
  Limited resources
  Weaknesses in protocols
Centralization is often unfeasible
Only local information
  No extra overhead
“Survive in the crowd” vs being fair
Decentralization
Potential Solutions
[1]
Time
  Scheduling
  CW adaptation
Frequency
  DSA
  DCB
Space
  TPC and CST adjustment
  Directional transmissions
  Interference cancellation
Coordinated
Uncoordinated

## Slide 6: Stateless Q-learning

## Slide 7: Stateless Q-learning
States in WNs are very complex to be defined. Each WN implements Stateless Q-learning by only considering actions.
Q(s,a) is updated through the reward and the tuning parameters:
  𝛼: learning rate
  𝛾: discount factor
The 𝜀-greedy policy is used to frame the exploration-explotaition trade-off
  𝜀0: initial exploration coefficient
Reinforcement Learning
Q-learning
Mapping to WNs
Actions are pairs of {Channel, Tx Power}
The reward ri(t) afterWNi plays an action is given by
RL is a ML technique that aims at optimizing action selection
Feedback received by the system is a scalar reward signal
Notes: Focus on a completely decentralized scenario: Described by the set of actions and rewards
  (as opposed to supervised learning where the system is told which the correct action was).
  Choose action with maximum “Q” with probability 1 – 𝜀. Otherwise, choose a random action
  𝜀0 decreases quadratically with the time

## Slide 8: Scenario and System Model

## Slide 9: Scenario and System Model
We consider a symmetric grid scenario containing 4 WNs. STAs are located to the most conservative position regarding the overlapping interference.
Dense deployment: 0.008 AP/m3
Limited resources:
Allows studying the adversarial setting on equal terms
  Channels: 1 and 2
  TX power levels: 5, 10, 15 and 20 dBm

## Slide 10: Simulation Results

## Slide 11: Analysis of the Input Parameters
Some combinations of {𝛼, 𝛾, 𝜀0} show results close to the throughput resulting from the optimal proportional fairness.
100 repetitions of 10,000 iterations*
* The last 5000 iterations are considered for plotting results (avoid the instability during the transitory regime)
There is a strong relationship between the discount factor (𝛾) and the learning rate (𝛼). For good performance, 𝛼 > 𝛾
Notes: Mention optimal configurations briefly
Mention that optimal solution (agg. Tpt) requires centralization
Mention that some configurations allow reaching the optimal fairness, and exploring not enough lead to variable results (from good to bad performacne)

## Slide 12: Actions Probability in each WN
More actions are explored as 𝜀0 increases
High {𝛼, 𝛾} also entails more exploration
Single simulation of 10,000 iterations
𝜀0 = 1, 𝛼 = 1, 𝛾 = 0.95
𝜀0 = 0.1, 𝛼 = 1, 𝛾 = 0.95
𝜀0 = 1, 𝛼 = 0.1, 𝛾 = 0.05
𝜀0 = 0.1, 𝛼 = 0.1, 𝛾 = 0.05
Notes: Mention that we now look into individual performance, and that we use different values of epsilon, alpha and gamma to see the networks behavior
In figure 1, mention that maximum exploration leads to channel swapping, as well as the individual reward is greedy
Previous phenomena is soften in Figure 2, where alpha and gamma are lower
Remark fast convergence in Figures 3 and 4, which does not lead to fair configurations

## Slide 13: Average Throughput experienced per WN
A higher fairness is noticed as 𝜀0 increases
A high {𝛼, 𝛾} pair entails a higher aggregate throughput
Single simulation of 10,000 iterations
𝜀0 = 1, 𝛼 = 1, 𝛾 = 0.95
𝜀0 = 0.1, 𝛼 = 1, 𝛾 = 0.95
𝜀0 = 0.1, 𝛼 = 0.1, 𝛾 = 0.05
𝜀0 = 1, 𝛼 = 0.1, 𝛾 = 0.05
Notes: * Fairness is achieved when enough exploration is provided

## Slide 14: Temporal Throughput experienced per WN
A higher variability is noticed as 𝜀0 increases
A high {𝛼, 𝛾} pair entails more variability
Single simulation of 10,000 iterations
𝜀0 = 1, 𝛼 = 1, 𝛾 = 0.95
𝜀0 = 0.1, 𝛼 = 1, 𝛾 = 0.95
𝜀0 = 1, 𝛼 = 0.1, 𝛾 = 0.05
𝜀0 = 0.1, 𝛼 = 0.1, 𝛾 = 0.05
Notes: Only mention that a higher exploration incurs into a higher temporal throughput variability, which may have side effects on the networks performance, as it may affect to higher protocols levels

## Slide 15: Conclusions

## Slide 16: Conclusions
Spatial Reuse can be improved in dense WNs
Decentralized learning
Entails competitiveness, becomes worse if a NE does not exist
Q-learning
Allows finding close-to-optimal configurations in terms of fairness
Trade-off between the individual throughput and the variability
1
2
Notes: The decentralized problem with limited resourced might not have a *pure strategy* equilibrium

## Slide 17: Implications of Decentralized Q-learning Resource Allocation in Wireless Networks

## Slide 18: Moving towards Artificial Intelligence
AI may satisfy the high-demanding requirements in next-generation scenarios. There is an upward trend in combining AI with Wireless Communications.
Previous Work
Q-learning
Packet routing [2]
Energy harvesting [3]
MABs
Rate sampling [4]
ANNs
AP selection [5, 6]
Challenges in WNs vs ML features
Adversarial setting
WNs strongly interact with the environment
High variability (channel, users, traffic…)
Observations-based learning process
Training a system may be infeasible and not practical
Optimal solution or an approximation

## Slide 19: Reinforcement Learning
An agent attempts to learn a policy given the observations it does. The goal is to maximize the expected future cumulative reward.
MDP formulation:
S: set of states
A: set of actions
Ra,s: reward
T(s, a, s’): transition probability
No supervisor (only reward signal)
Delayed feedback & sequentiality
Actions affect the environment
Examples:
Q-learning, SARSA, TD-learning

## Slide 20: Q-learning [7]
Agents maintain an estimate of the expected long-term discounted reward for each state-action pair. The goal is to maximize the long-term reward.
Update rule:
  rt = obtained reward
  𝛼t = learning rate
  𝛾 = discount factor
𝜀-greedy policy (select the most rewarding action with probability 1 - 𝜀)
Previous work:
  Real-time Q-learning for DCA [8]
  Q-learning for channel selection in mobile communications [9, 10]

## Slide 21: Stateless Q-learning Algorithm

## Slide 22: System Model
Throughput calculation is done through interference, so that performance enhancement can be achieved through interference minimization.
Throughput computed according to the Shannon’s capacity
Indoor path-loss model
Possible actions:
  Channels: 1 and 2 (with co-channel interference)
  TX power levels: 5, 10, 15 and 20 dBm

## Slide 23: Optimal Configuration
For comparison purposes, we compute the optimal configurations that maximize the aggregate throughput and the proportional fairness, respectively.
Aggregate throughput
One combination is {a1, a1, a7, a8}*
Two WNs sacrifice their individual performance for the “common good”
Proportional fairness
One combination is {a7, a8, a7, a8}
Aggressive configurations
*Actions indexes are mapped to {channel number, tx power (dBm)}:
a1={1,5}, a2={2,5}, a3={1,10}, a4={2,10},
a5={1,15}, a6={2,15}, a7={1,20}, a8 ={2,20}

## Slide 24: References
[1] Afaqui, M. S., Garcia-Villegas, E., Lopez-Aguilera, E., & Camps-Mur, D. (2016, May). Dynamic sensitivity control of access points for IEEE 802.11 ax. In Communications (ICC), 2016 IEEE International Conference on (pp. 1-7). IEEE.
[2] Littman, M., & Boyan, J. (1993, July). A distributed reinforcement learning scheme for network routing. In Proceedings of the international workshop on applications of neural networks to telecommunications (pp. 45-51). Psychology Press.
[3] Miozzo, M., Giupponi, L., Rossi, M., & Dini, P. (2015, June). Distributed Q-learning for energy harvesting Heterogeneous Networks. In Communication Workshop (ICCW), 2015 IEEE International Conference on (pp. 2006-2011). IEEE.
[4] Combes, R., Proutiere, A., Yun, D., Ok, J., & Yi, Y. (2014, April). Optimal rate sampling in 802.11 systems. In INFOCOM, 2014 Proceedings IEEE (pp. 2760-2767). IEEE.
[5] Bojovic, B., Baldo, N., Nin-Guerrero, J., & Dini, P. (2011, December). A supervised learning approach to cognitive access point selection. In GLOBECOM Workshops (GC Wkshps), 2011 IEEE (pp. 1100-1105). IEEE.
[6] Bojovic, B., Baldo, N., & Dini, P. (2012, January). A neural network based cognitive engine for IEEE 802.11 WLAN access point selection. In Consumer Communications and Networking Conference (CCNC), 2012 IEEE (pp. 864-868). IEEE.
[7] Sutton, Richard S. "Learning to predict by the methods of temporal differences." Machine learning 3.1 (1988): 9-44.
[8] Nie, J., & Haykin, S. (1999). A Q-learning-based dynamic channel assignment technique for mobile communication systems. IEEE Transactions on Vehicular Technology, 48(5), 1676-1687.
[9] Li, H. (2009, October). Multi-agent Q-learning of channel selection in multi-user cognitive radio systems: A two by two case. In Systems, Man and Cybernetics, 2009. SMC 2009. IEEE International Conference on (pp. 1893-1898). IEEE.
[10] Bennis, M., & Niyato, D. (2010, December). A Q-learning based approach to interference avoidance in self-organized femtocell networks. In GLOBECOM Workshops (GC Wkshps), 2010 IEEE (pp. 706-710). IEEE.